## Slide 1: COMP821 semester 1 2024
Internet of Things (IoT) Security

## Slide 2: Internet of Things (IoT)
What is the Internet of Things (IoT)?
“The pervasive interconnectivity of various devices communicating and exchanging data with one another. “
IoT can be used to support scenarios where objects, animals or people are provided with unique identifiers
and with the ability to transfer data over a network without requiring human-to-human or human-to-computer interaction
IoT is network of physical objects which contain embedded technology to communicate
    and sense or interact with their internal states or the external environment

## Slide 3
IoT Technology Drivers
  Wireless Sensor Networks (WSN)
  Radio Frequency Identification (RFID)
  Enable connecting machine to machine (M2M), human to human (H2H), human to machine (H2M) while providing ease of communication, identification, management and control among the devices ‘
  The proliferation of M2M devices across the globe.
Characteristics of IoT devices
Have built in sensing and communication interfaces such as:
Bluetooth,
Sensors,
RFID,
GPS,
Infrared sensors,
Laser scanners,
Actuators,
Wireless LANs
Local Area Networks (LANs)
Evans, 2011
Notes: Evans, D. (2011). The internet of things: How the next evolution of the internet is changing everything. CISCO white paper, 1(2011), 1-11.
Zhao, K., & Ge, L. (2013, December). A survey on the internet of things security. In 2013 Ninth International Conference on Computational Intelligence and Security (pp. 663-667). IEEE.
Kai, K. A. N. G., PANG, Z. B., & Cong, W. A. N. G. (2013). Security and privacy mechanism for health internet of things. The Journal of China Universities of Posts and Telecommunications, 20, 64-68

## Slide 4: Internet of Things Examples
http://www.libelium.com/top_50_iot_sensor_applications_ranking/
Smart Cities (Smart parking, Traffic congestion)
Retail (intelligent shopping, NFC payment)
Logistics (quality of shipment conditions, item location)
Industrial Control (M2M apps, indoor asset location RFID)
Smart Agriculture (Green houses, Wine quality)
Smart Animal Farming (Animal Tracking, Toxic Gas emissions)
Domestic (Energy & water use, Remote control)
Ehealth (Patient Surveillance, UV radiation)
Opportunities for IoT
  Wildlife monitoring
  Environmental monitoring (pollution, water reservoir observation)
  E-health systems and monitoring
  ITS (Intelligent Transportation System)
  Smart grids

## Slide 5: IoT & Big Data

## Slide 6: IoT Architecture

## Slide 7
A three-layer architecture defined by functions (Miao et al., 2012)
  Perception layer
  The network layer
  The application layer
Internet of Things three-tier architectural layer
Notes: i. Perception Layer
The perception layer is the sense organ of IoT. It aims at recognizing objects and gathering information. This layer includes RFID tags, 2-D barcode labels and readers, terminals, GPS, camera, sensors and sensor network.
ii. The network layer
This layer represents the nucleus of IoT. It processes and transmits information received from the perception layer to the application layer. The network layer comprises of the following; information center, intelligent processing center, Internet network systems and network management center.
iii. The Application Layer
This layer is a fusion of IoT’s socio-business requirements in order to realize the in-depth system processes. This layer represents the confluence of IoT and industrial technology with a mix of industrial needs and system processes. Though the IoT is still in its infancy and many researchers still consider it a “cloud-castle” as it is still in its formative stage and does not yet have a definite form (Holler & Tsiatsis, 2014). As advised by (Holler & Tsiatsis, 2014), the two-system structure of IoT namely; the Internet, and the communications network should be analyzed in order to gain better understanding of IoT and hence create a better architecture for the Internet of Things.

## Slide 8
Khan et al, 2018
Fig. 2. Common IoT standards and protocols.
Notes: Khan, M. A., & Salah, K. (2018). IoT security: Review, blockchain solutions, and open challenges. Future Generation Computer Systems, 82, 395-411.

## Slide 9
Azrour et al., 2021
Notes: The processing layer is also recognized as the middleware layer. It is responsible for controlling, analyzing, processing, and storing received data. It can make decisions according to the processing data without human intervention. 'is layer benefits from existing solutions including cloud computing, big data, and databases.
The business layer has a responsibility to manage the whole IoT systems. Its role is to control applications, business, and profit models. Furthermore, the users’ privacy can be managed by this layer.
Azrour, M., et al. (2021). "Internet of things security: challenges and key issues." Security and Communication Networks 2021: 1-11.

## Slide 10
Ahmid et al, 2023
Notes: Ahmid, M. and O. Kazar (2023). "A comprehensive review of the internet of things security." Journal of Applied Security Research 18(3): 289-305.

## Slide 11: IoT Security
PRE-ASSIGNED READINGS
1. Ahmid, M. and O. Kazar (2023). "A comprehensive review of the internet of things security." Journal of Applied Security Research 18(3): 289-305.
2. Kouicem, D. E., et al. (2018). "Internet of things security: A top-down survey." Computer Networks 141: 199-221.

## Slide 12
Security in IoT
IoT has specific security requirements
More complicated due to:
  Concerns about the safety of the routing information
  Information payload traverses heterogeneous and lossy wireless networks
  Some devices do not have a conventional user interface and are placed in physically unprotected and unattended environments
  Security solutions have to be affordable for constrained IoT devices
Notes: More complicated due to the safety of routing information and information payload that will traverse heterogeneous networks of billions of devices in wired and wireless forms.
IOT security challenges: Zhao, K., & Ge, L. (2013, December). A survey on the internet of things security. In 2013 Ninth International Conference on Computational Intelligence and Security (pp. 663-667). IEEE
IOT Challenges Kouicem, D. E., et al. (2018). "Internet of things security: A top-down survey." Computer Networks 141: 199-221.

## Slide 13
Notes: Zhao, K., & Ge, L. (2013, December). A survey on the internet of things security. In 2013 Ninth International Conference on Computational Intelligence and Security (pp. 663-667). IEEE

## Slide 14: IoT Security Requirements and Solutions
KOUICEM ET AL., 2018
Notes: Kouicem, D. E., et al. (2018). "Internet of things security: A top-down survey." Computer Networks 141: 199-221.

## Slide 16
Notes: See article for detail

## Slide 18: IoT Security features and an An attack taxonomy
AHMID et al., 2023
Notes: Ahmid, M. and O. Kazar (2023). "A comprehensive review of the internet of things security." Journal of Applied Security Research 18(3): 289-305.

## Slide 20
Ahmid et al, 2023
Notes: Ahmid, M. and O. Kazar (2023). "A comprehensive review of the internet of things security." Journal of Applied Security Research 18(3): 289-305.

## Slide 24: ENTER AI
Ahmad, R., Wazirali, R., & Abu-Ain, T. (2022). Machine learning for wireless sensor networks security: An overview of challenges and issues. Sensors, 22(13), 4730.
Alwahedi, F., Aldhaheri, A., Ferrag, M. A., Battah, A., & Tihanyi, N. (2024). Machine learning techniques for IoT security: Current research and future vision with generative AI and large language models. Internet of Things and Cyber-Physical Systems.
Ni, C., & Li, S. C. (2024). Machine learning enabled Industrial IoT Security: Challenges, Trends and Solutions. Journal of Industrial Information Integration, 100549.
Ali, H. H., Naif, J. R., & Humood, W. R. (2024, March). Deep learning algorithms for IoT security (survey). In AIP Conference Proceedings (Vol. 2885, No. 1). AIP Publishing.